## Slide 1
Python script for selection of multistage harmonic indices
-
Instructions
November 3rd, 2023

## Slide 2: Step 1: Python environment
Install any Python IDE. VS Code is used for demo, here
Run the Python script HI_Choice.py from your IDE.
VS Code Run button

## Slide 3: Step 2: user inputs
In the Python script, enter the required inputs:
Geometry: # of sectors of each stage
Main harmonic index for the response, which depends on engine order of interest
Connection table (Optional)
  For each stage in the order that the stages are entered in N_sectors entry, indicate the connections of stages
  In this example, the 11-sector stage is connected to the 10-sector and 13-sector stages; the 10 and 13-sector stages are only connected to the 11-sector stage

## Slide 4: Step 2: user inputs
In the Python console, enter the optional inputs and press the Enter key after each input:
Do you want to use a connectivity table? (only for more than 2 stages)
  Use of the connectivity table will account for the proximity of stages when deciding the influence that a harmonic index (HI) may have on a given stage.
Do you want to compute additional HIs? If yes, two methods:
  1st extension of fundamental nodal diameters: extends the fundamental nodal diameters coupling method up to the input maximum nodal diameter
  All couplings: provides all couplings below the input maximum nodal diameter
  If yes, input the maximum # of Nodal diameters:
  A low number will select a minimal number of HIs, which is computationally efficient but gives accurate results for a smaller frequency range.
  A high number will select more HIs and produce more accurate results over a wider frequency range at the price of higher computation costs.

## Slide 5: Step 3: script outputs
Outputs are printed in the console:
If no additional harmonic indices, only fundamental nodal diameters coupling
If additional harmonic indices, and 1st extension of fundamental nodal diameters method is selected
If additional harmonic indices, and all couplings method is selected

## Slide 6: Examples
Example 1 - Engine order 1 response – fundamental nodal diameters
Example 2 - Engine order 1 response - 1st extension of fundamental nodal diameters
With low maximum nodal diameter

## Slide 7: Examples
Example 3 - Engine order 1 response - 1st extension of fundamental nodal diameters
With high maximum nodal diameter
Example 4 - Engine order 1 response – all couplings With high maximum nodal diameter